INSTRUCTIONS AND WARRANTY

MODEL NO. RHMN20L

# RUSSELL HOBBS 20L MANUAL MICROWAVE OVEN

Congratulations on purchasing our Russell Hobbs 20L Manual Microwave Oven. Each unit is manufactured to ensure safety and reliability. Before using this appliance for the first time, please read the instruction manual carefully and keep it for future reference.

FEATURES OF THE RUSSELL HOBBS 20L MANUAL MICROWAVE OVEN

- 20L Capacity

- Elegant mirror finish front

- Power output: 700W

- 255mm glass turntable diameter

- 5 power levels

- 35 minute cooking timer with end signal

- Defrost function

- User friendly manual control panel with rotary timer

- Easy to use pull-handle door

- Door safety lock

- Enamel interior for easy cleaning

- For domestic use only

- 2 year warranty (1 year retail • 1 year extended upon online registration of product • visit www.russellhobbs.co.za)

# SPECIFICATIONS

| Power Consumption: | 230V~50Hz 1050W (Microwave) |
| --- | --- |
| Output: | 700W |
| Operation Frequency: | 2450MHz |
| Outside Dimensions: | 258.2mm (H) x439.5 mm (W) x 335mm (D) |
| Oven Cavity Dimensions: | 208.2mm(H)×306mm(W)×306.6mm(D) |
| Oven Capacity: | 20 Litres |
| Cooking Uniformity: | 255mm Diameter Turntable System |
| Net Weight: | Approx.11.2kg |

## IMPORTANT SAFEGUARDS

When using any electrical appliance, basic safety precautions should always be followed including the following:

- Please read the instructions carefully before using any appliance.

- Always ensure that the voltage on the rating label corresponds to the mains voltage in your home.

- Incorrect operation and improper use can damage the appliance and cause injury to the user.

- The appliance is intended for household use only. Commercial use invalids the warranty and the supplier can not be held responsible for injury or damage caused when using the appliance for any other purpose than that intended.

- Avoid any contact with moving parts.

- Close supervision is required when any appliance is used near or by children.

- Only allow children to use the oven without supervision when adequate instructions have been given so that the child is able to use the oven in a safe way and understands the hazards of improper use.

- This appliance is not intended for use by persons with reduced physical, sensory or mental capabilities, or lack of experience and knowledge, unless they have been given supervision or instruction concerning use of the appliance by a person responsible for their safety.

- Check the power cord and plug regularly for any damage. If the cord or the plug is damaged, it must be replaced by the manufacturer or a qualified person in order to avoid an electrical hazard.

- Do not use the appliance if it has been dropped or damaged in any way. In case of damage, take the unit in for examination and/or repair by an authorised service agent.

- Do not operate the oven when empty.

- Do not use the Microwave oven for storage purposes. Do not leave paper products, cooking utensils or food in the cavity when not in use.

- To reduce the risk of fire in the oven cavity:

- When heating food in a plastic or paper container, check the oven frequently in terms of the possibility of ignition.

- Remove wire twist-ties from paper or plastic bags before placing the bag in the oven.

- If smoke is observed, switch off or unplug the appliance and keep the door closed in order to stifle any flames.

WARNING: Liquid or other food must not be heated in sealed containers since they are able to explode.

15. Microwave heating of beverages can result in delayed eruptive boiling; therefore, care has to be taken when handling the container.

16. Do not fry food in the oven. Hot oil can damage oven parts and utensils and even result in burns.

17. Eggs in their shell and whole hard-boiled eggs should not be heated in microwave ovens since they may explode even after microwave heating has ended.

18. Pierce foods with heavy skins such as potatoes, whole squashes, apples and chestnuts before cooking.

19. The contents of feeding bottles and baby jars should be stirred or shaken, and the temperature should be checked before serving in order to avoid burns or scalding.

20.Cooking utensils may become hot because of heat transferred from the heated food. Potholders / oven gloves may be needed when handling utensils.

21. Utensils should be checked to ensure that they are suitable for use in the microwave oven.

22. It is hazardous for anyone other than a trained person to carry out any service or repair operation which involves the removal of any cover which gives protection against exposure to microwave energy.

- This product is Group 2 Class B ISM equipment. The definition of Group 2 which contains all ISM (Industrial, Scientific and Medical) equipment in which radio-frequency energy is intentionally generated and/or used in the form of electromagnetic radiation for the treatment of material, and spark erosion equipment. For Class B equipment is equipment suitable for use in domestic establishments and in establishments directly connected to a low voltage power supply network which supplies buildings used for domestic purpose.

- Never immerse the unit in water or any other liquid for cleaning purposes.

- Remove the plug from the socket by gripping the plug. Do not pull on the cord to disconnect the appliance from the mains. Always unplug the unit when not in use, before cleaning or when adding or removing parts.

- The use of accessory attachments that are not recommended or supplied by the manufacturer may result in injuries, fire or electric shock.

- Use of an extension cord with this appliance is not recommended. However, if it is necessary to use an extension lead, ensure that the lead is suited to the power consumption of the appliance to avoid overheating of the extension cord, appliance or plug point.

- Do not place the extension cord in a position where it can be pulled on by children or animals or tripped over.

- Do not allow the cord to touch hot surfaces and do not place the microwave oven on or near a hot gas or electric burner or in a heated oven.

- This appliance is not suitable for outdoor use. Do not use this appliance for anything other than its intended use.

- Do not carry the appliance by the power cord.

- Do not leave this appliance unattended during use. Always unplug the unit when not in use or before cleaning.

- Always operate the appliance on a smooth, even, stable surface.

- The manufacturer does not accept responsibility for any damage or injury caused by improper or incorrect use, or for repairs carried out by unauthorised personnel.

- The microwave oven should not be placed in a cabinet unless it has been tested in a cabinet.

- Appliances are not intended to be operated by means of an external timer or separate remote-control system.

- The door or the outer surface may get hot when the appliance is in operation.

- The rear surface of the appliance should be placed against a wall.

- Failure to comply with the above-mentioned pre-cautions and instructions, could affect the safe operation of this machine.

- Do not attempt to operate this oven with the door open since open door operation can result in harmful exposure to microwave energy. It is important not to break or tamper with the safety interlocks.

- Do not place any object between the oven front face and the door or allow soil or cleaner residue to accumulate on sealing surfaces.

- Do not operate the oven if it is damaged. It is particularly important that the oven door close properly and that there is no damage to the

Door (bent),

Hinges and latches (broken or loosened),

Door seals and sealing surfaces.

- PLEASE TAKE NOTE - If the microwave appliance is not maintained in a good state of cleanliness, its surface could become degraded, its lifespan affected and could result in a possibly hazardous situation.

- In case of technical problems, switch off the machine and do not attempt to repair it yourself. Return the appliance to an authorised service facility for examination, adjustment or repair. Always insist on the use of original spare parts.

INSTALLATION

- Make sure that all the packing materials are removed from the inside of the door.

- WARNING: Check the oven for any damage, such as misaligned or bent door, damaged door seals and sealing surface, broken or loose door hinges and latches and dents inside the cavity or on the door. If there is any damage, do not operate the oven and contact qualified service personnel.

- This microwave oven must be placed on a flat, stable surface to hold its weight and the heaviest food likely to be cooked in the oven.

- Do not place the oven where heat, moisture, or high humidity are generated, or near combustible materials.

- For correct operation, the oven must have sufficient airflow. Allow 20cm of space above the oven, 20cm at back and 20cm at both sides. Do not cover or block any openings on the appliance. Do not remove feet.

- Do not operate the oven without a glass tray, roller support, and shaft in their proper positions.

- Make sure that the power supply cord is undamaged and does not run under the oven or over any hot or sharp surface.

- The socket must be readily accessible so that it can be easily unplugged in an emergency.

- Blocking the intake and/or outlet openings can damage the oven.

- Remove any protective film found on the microwave cabinet surface.  Do not remove the light brown Mica cover that is attached to the oven cavity to protect the magnetron.

- Never place the glass tray upside down. The glass tray should never be restricted.

- Both glass tray and turntable ring assembly must always be used during cooking.

- All food and containers are always to be placed on the glass tray for cooking.

- If the glass tray or turntable ring assembly cracks or breaks, contact your nearest authorised service center.

TURNTABLE INSTALLATION

PARTS DIAGRAM

- Door lock - Microwave oven door must be properly closed in order for it to operate

- Viewing window - Allow user to see the cooking status

- Rotating ring - The glass turntable sits on its wheels; it supports the turntable and helps it to balance when rotating

- Rotating axis - The glass turntable sits on the axis; the motor underneath it drives the turntable to rotate

- Turntable - The food sits on the turntable, its rotation during operation helps to cook food evenly

NOTE: Put the rotating ring in first and then fit the turntable onto the rotating axis- make sure that it is geared in properly

- Control panel - See below in details

- Outer cover- Used for wrapping and protecting the internal structural parts and electrical components of the whole machine

- Waveguide cover - It is inside the microwave oven, next to the wall of control panel. 
WARNING: Never remove the waveguide cover

OPERATING THE CONTROL PANEL

1. CLOCK SETTING

The maximum setting is 35 minutes, there is a ringtone at the end, and the knob returns to the “0” position.

2. MICROWAVE FUNCTION

Five power levels:

| HIGH | 100% power output | (Quick cooking) |
| --- | --- | --- |
| M.High | 80% power output | (Normal cooking) |
| Med | 55% power output | (Slow cooking) |
| M.Low | 30% power output | (Defrost food) |
| LOW | 17% power output | (Keep warm) |

Defrosting guide

|  | Weight | Defrost time |
| --- | --- | --- |
| Meat | 0.1~1.0kg | 1:30~26:00 |
| Poultry | 0.2~1.0kg | 2:30~22:00 |
| Sea food | 0.1~0.9kg | 1:30~14:00 |

# OPERATING INSTRUCTIONS

- Before connecting the cord, make sure the timer is set to “0” position.

- Turn the power knob clockwise to set the desired power level. - The amount of time can be followed as per your cooking guide or chosen recipe.

- The microwave oven will automatically start cooking after the power level and cooking cycle time are set. - If pausing in between is needed, just open the door at any time, and close it to resume operation.

- Once the cooking cycle time has finished, the unit will make a “beep” sound and the light in the Microwave will turn off

- Always set the time to “0” when the unit is not in use.

# RADIO INTERFERENCE

# Operation of the microwave oven can cause interference to your radio, TV, or similar equipment.  When there is interference, it may be reduced or eliminated by taking the following measures:

- Clean the door and sealing surface of the oven.

- Reposition the receiving antenna of the radio or television.

- Relocate the microwave oven with respect to the receiver.

- Plug the microwave oven into a different outlet so that microwave oven and receiver are on different branch circuits.

# MICROWAVE COOKING PRINCIPLES

- Arrange food carefully. Place thickest areas towards outside of dish.

- Watch cooking time. Cook for the shortest amount of time indicated and add more as needed. Food severely overcooked can smoke or ignite.

- Cover foods while cooking. Covers prevent spattering and help foods to cook evenly.

- Turn foods over once during microwave cooking to speed cooking of such foods as chicken and hamburgers. Large items like roasts must be turned over at least once.

- Rearrange foods such as meatballs halfway through cooking both from top to bottom and from the center of the dish to the outside.

# UTENSILS GUIDE

  - The ideal material for a microwave utensil is material that is transparent.  This allows energy to pass through the container and heat the food.

  - A microwave cannot penetrate metal, so metal utensils or dishes with metallic trim should not be used.

  - Do not use recycled paper products when cooking in the microwave, as they may contain small metal fragments which may cause sparks and/or fires.

  - Round /oval dishes rather than square/oblong ones are recommended, as food in corners tends to overcook.

  - Narrow strips of aluminium foil may be used to prevent overcooking of exposed areas.

The list below is a general guide to help you select the correct utensils:

| COOKWARE | MICROWAVE |
| --- | --- |
| Heat–Resistant Glass | Yes |
| Non Heat–Resistant Glass | No |
| Heat–Resistant Ceramics | Yes |
| Microwave–Safe Plastic Dish | Yes |
| Paper Kitchen Towels | Yes |
| Metal Tray | No |
| Metal Rack | No |
| Aluminium Foil & Foil Containers | No |
| Parchment Paper | Yes |
| Plastic Wrap | Yes |
| Wax Paper | Yes |
| Containers containing metal parts | No |
| Metal Twist-ties | No |
| Paper Bags | No |
| Plastic Foam | No |
| Wood | No |

COOKING GUIDE

| Function/Power | Power Output | Application |
| --- | --- | --- |
| Low | 17% micro. | Soften ice cream |
| Med. Low (Defrost) | 33% micro. | Soup stew, soften butter or defrost |
| Med. | 55% micro. | Stew, fish |
| Med. High | 77% micro. | Rice, fish, chicken, mince |
| High | 100% micro. | Reheat, milk, boil water, vegetables, heat beverages |

Notice:   When removing food from the oven, please ensure that the oven power is switched off by turning the timer switch to 0 (zero).  Failure to do so, and operating the microwave oven without food in it, can result in overheating and damage to the magnetron.

TROUBLE SHOOTING

| NORMAL |
| --- |
| Dim oven light | During cooking with low microwave power, the oven light may become dim. It is normal. |
| Steam accumulating on door/ hot air out of vents | Foods may generate steam during the cooking process. Most steam will escape via the vents however some may accumulate on the oven door. This is normal. Wipe with soft cloth one Microwave cooled down. |

| ISSUE | POSSIBLE CAUSE | SOLUTION |
| --- | --- | --- |
| Microwave does not start up | Power cord not plugged in correctly | Unplug. Then plug in again after 10 seconds |
|  | Fuse blowing or circuit breaker works | Replace the fuse or reset the circuit breaker (to be repaired by HOLB Service Department) |
|  | Trouble with the power outlet | Test the power outlet with other electrical appliances |
| Microwave does not heat | The door is not closed properly | Close the door well |
| Glass turntable makes noise when microwave is in operation | Dirty roller and cavity bottom | Refer to “Cleaning and Maintenance” section below to clean dirty or soiled parts. |

CLEANING AND MAINTENANCE

- Do not open or change any parts by yourself. Please refer to a qualified electrical service department or return to the supplier if servicing is necessary.

- Turn off the oven and remove the power plug from the wall socket before cleaning.

- Keep the inside of the oven clean. When food splatters or spilled liquids adhere to oven walls, wipe with a damp cloth. Mild detergent may be used if the oven gets very dirty. NOTE: Avoid the use of spray and other harsh cleaners as they may stain, streak or dull the door surface.

- The outside surfaces should be cleaned with a damp cloth. To prevent damage to the operating parts inside the oven, water should not be allowed to seep into the ventilation openings.

- Wipe the door and window on both sides, the door seals and adjacent parts frequently with a damp cloth to remove any spills or spatters. Do not use abrasive cleaner.

- Do not allow the control panel to become wet. Clean with a soft, damp cloth. When cleaning the control panel, leave oven door open to prevent oven from accidentally turning on.

- If steam accumulates inside or around the outside of the oven door, wipe with a soft cloth. This may occur when the microwave oven is operated under high humidity condition. And it is normal.

- It is occasionally necessary to remove the glass tray for cleaning. Wash the tray in warm sudsy water or in a dishwasher.

- The roller ring and oven floor should be cleaned regularly to avoid excessive noise. Simply wipe the bottom surface of the oven with mild detergent. The roller ring may be washed in mild sudsy water or dishwasher. When removing the roller ring from cavity floor for cleaning, be sure to replace in the proper position.

- Remove odors from your oven by combining a cup of water with the juice and rind of one lemon in a deep microwaveable bowl, microwave for 5 minutes. Wipe thoroughly and dry with a soft cloth.

- When it becomes necessary to replace the oven light, please consult a dealer to have it replaced.

- The oven should be cleaned regularly and any food deposits removed. Failure to maintain the oven in a clean condition could lead to deterioration of the surface that could adversely affect the life of the appliance and possibly result in a hazardous situation.

- Please do not dispose this appliance into the domestic rubbish bin; it should be disposed to the particular disposal center provided by the municipalities.

- Do not use bleach or other abrasive substance or solvents to clean your appliance as it can be damaging to the finish.

STORING THE APPLIANCE

- Unplug the unit from the wall outlet and clean all the parts as instructed above. Ensure that all parts are dry before storing.

- Store the appliance in its box or in a clean, dry place.

- Never store the appliance while it is still wet or dirty.

- Never wrap the power cord around the appliance.

SERVICING THE APPLIANCE

There are no user serviceable parts in this appliance. If the unit is not operating correctly, please check the following:

- You have followed the instructions correctly

- That the unit has been wired correctly and that the wall socket is switched on.

- That the mains power supply is ON.

- That the plug is firmly in the mains socket.

If the appliance still does not work after checking the above:

- Consult the retailer for possible repair or replacement. If the retailer fails to resolve the problem and you need to return the appliance, make sure that:

- The unit is packed carefully back into its original packaging.

- Proof of purchase is attached.

- A reason is provided for why it is being returned.

If the supply cord is damaged, it must be replaced by the manufacturer or an authorised service agent, in order to avoid any hazard. If service becomes necessary within the warranty period, the appliance should be returned to an approved Amalgamated Appliance (Pty) Ltd service centre. Servicing outside the warranty period is still available, but will, however, be chargeable.

CHANGING THE PLUG

Should the need arise to change the fitted plug, follow the instructions below.

This unit is designed to operate on 230V~240V current only. Connecting to other power sources may damage the appliance.  Connect a three-pin plug as follows:

The wires in this mains lead are coloured in accordance with the following code:

Green/Yellow	= Earth

Blue		= Neutral

Brown		= Live

According to the Waste of Electrical and Electronic Equipment (WEEE) directive, WEEE should be separately collected and treated.  If at any time you need to dispose of this product, please do NOT dispose of this product with household waste.  Please send this product to WEEE collecting points where available.